## Slide 1
Automated Room Occupancy-Based Light and Fan Control System
Team Members:
K.A.P.R.Kaluarachchi (240313D)
M.G.A.S.Karunananda (240325P)
W.A.M.S.Karunarathne (240333M)
R.R.Karunaratna (240334R)

## Slide 2: Problem Addressed
• Lights and fans are often left switched ON even when the room is empty.
• This leads to unnecessary electricity wastage.
• Manual switching is unreliable in shared spaces.
Goal: Create a system that turns appliances ON only when people enter and OFF when nobody is inside.

## Slide 3: Objective
Our main objectives were:
• Detect humans automatically using YOLO.
• Track their movement direction (IN or OUT).
• Maintain an accurate occupancy count.
• Control lights and fans based on this count.
• Reduce energy waste through smart automation.

## Slide 4: System Overview
The system consists of:
• Raspberry Pi as the main controller.
• Ultrasonic sensors to detect approaching people.
• Camera activated only when sensors detect motion.
• YOLO model to detect persons inside video frames.
• Relay module to switch lights and fan ON/OFF.
The Pi processes a short video using one CPU core to determine entry or exit.

## Slide 5: Detection & Tracking
1. Ultrasonic sensors first detect movement near the door.
2. Raspberry Pi activates the camera and records a short video.
3. YOLO detects persons in selected frames.
4. The camera view is divided into IN and OUT zones.
5. The system tracks the person’s centroid across these zones:
• OUT → IN = Entry (+1)
• IN → OUT = Exit (–1, not below zero)
6. Only essential frames are processed to reduce CPU load.

## Slide 6: Control Logic
• The system maintains an integer 'occupancy_count'.
• When occupancy_count changes from 0 → 1:
→ Relay turns ON lights and fan.
• When occupancy_count changes from 1 → 0:
→ Relay turns OFF all appliances.
This ensures appliances operate only when needed.

## Slide 7: Final Outcome & Evaluation
• The system worked reliably under normal lighting conditions.
• Entry and exit detection achieved over 85% accuracy.
• Relay switching was instantaneous and stable.
• Ultrasonic-triggered camera activation reduced processing load.
• Minor issues occurred when multiple people crossed simultaneously.

## Slide 8: Future Improvements
• Add multi-person tracking (SORT/DeepSORT) to reduce miscounts.
• Use optimized YOLO models for faster detection.
• Add PIR/thermal sensors for better low-light performance.
• Add IR break-beam sensors for more precise doorway detection.
• Implement mobile app monitoring.
• Use Coral TPU for real-time high-speed processing.